| Register name | Address offset | Access type | description | VHDL name |
| --- | --- | --- | --- | --- |
| PHASE_TABLE | 0x000000 (reg0) | RW | 23 – write enable (active high) 19..16 – data 12..0 – address | write_enable phase_data_in phase_addr_in |
| SPI_CONFIG | 0x000004 (reg1) | RW | 11 – ADC reset 10 - clock manager CS 9 - ADC4 CS 8 – ADC3 CS 7 – ADC2 CS 6 – ADC1 CS 5 - SPI DATA 4 – SPI CLK 3 – clock manager FUNC 2 – enable 125MHz clock 1 – enable 106MHz clock 0 – enable ADC generator | ADC_RESET_o spi_cs_ckm_pad_o spi_cs_adc4_pad_o spi_cs_adc3_pad_o spi_cs_adc2_pad_o spi_cs_adc1_pad_o spi_data_pad_o spi_clk_pad_o spi_func_pad_o sys_clk125_en_pad_o sys_clk106_en_pad_o vcxo |
| INIT_FREQ | 0x000008 (reg2) | RW | 31..0 - Initial frequency for PLL | freq_init |
| LOOP_CONFIG | 0x00000C (reg3) | RW | 24..16 – initial phase (azimuth) 7..4 – loop gain (0x0 :/1..0xF:/65535) 2 – DDS frequency limitation enable 1 - loop control: 0x1 = open | ph_init loop_gain loop_ctrl |
| DDS_FREQ_MIN | 0x000010 (reg4) | RW | 31..0 – min DDS frequency boundary | dds_freq_min |
| DDS_FREQ_MAX | 0x000014 (reg5) | RW | 31..0 – max DDS frequency boundary | dds_freq_max |
| FREV_GAIN | 0x000018 (reg6) | RW | 13..0 – revolution frequency gain | frev_gain |
| LO_SEL_DELAY | 0x00001C (reg7) | RW | 7..0 – number of turns till LO source switching | LO_delay |
| TAB_PT_ST | 0x000020 (reg8) | R | 29..28 – ST table address pointer 25..24 – INJ table address pointer 21..16 – C table address pointer 13..0 – HC table address pointer | ST_tab_ST_addr INJ_tab_ST_addr C_tab_ST_addr HC_tab_ST_addr |
| DRAM_PT_ST | 0x000024 (reg9) | R | DPRAM address at ST trigger | SDRAM_ST_addr |
| INJ_PT_TAB | 0x000100- 0x000103 | R | 31..0 – injection trigger pointers table | INJ_TAB_RD_DAT |
| HC_PT_TAB | 0x000200-0x00023F | R | 31..0 – HC trigger pointers table | C_TAB_RD_DAT |
| ST_PT_TAB | 0x000300- 0x000303 | R | 31..0 – ST trigger pointer table | ST_TAB_RD_DAT |
| C_PT_TAB | 0x010000- 0x011FFF | R | 31..0 – C trigger pointer table | C_TAB_RD_DAT |