Idea for Phase/Switch Table

Name	Bit	Description
FRefSel	0	Selects the FREF timing input or the ADC Sigma as the frequency reference to lock on-to. This changes the both the input reference source, and which of PllFRef or PllFRefHarmonic to use as the feed back signal in the PLL.
PllFRef	1	Phase table to synchronise to FREF
PllFRefHarmonic	2	Phase table to synchronise to Harmonic number * FREF ie Sigma
Gate	3	Gate signal for data integration
Blr	4	Base line restore signal
Acquire	5	Acquire data signal
Spare0	6
Spare1	7

The Phase table would have 16 x 512 entries and thus be 16 x 512 bytes long.
On each timing signal transition the phase table would increment to the next Phase table in the array.