Project	CERN-TMS
Date	2006-10-19
Reference	Cern-tms/pupe-api
Version	0.2 Preliminary
Author	Dr Terry Barnaby

# References
- IT-3384/AB: Technical Specification for a new trajectory measurement system for the CERN Proton Synchrotron.
- Alpha Data’s TMS Tender “pre-design-1.5”.
- Emailed questions answered by Jeroen Belleman of CERN.
- Visit to CERN on 2006-06-20
# Introduction
This PUPE API document concerns the API between the PUPE FPGA firmware and the software running on the Module controllers.
# Overview
The TMS operates in cycles lasting up to 2 seconds in time. The start of a cycle is initiated by the CYCLE_START timing signal input the cycle is terminated by the CYCLE_STOP timing signal. A cycle number counter is incremented on the start of a cycle. A C-timer counter is zeroed on the start of cycle and is incremented every 1ms. The 10MHz System clock is used as a reference for this. Thus all data timings have a Cycle Number and a time in ms from the start of cycle. The actual timing of data capture depends on the timing of the particle beam passing the PU in the Proton Synchrotron. The captured data is stored in a circular data buffer. A separate timing table points to entries in this table.
Each PUPE implements 3 Pick-Up processing channels. Each of these runs predominantly independent from each other.
# Control and Status Registers
The control and status registers are mapped into memory. Each register is 32bits wide and is situated on a 64bit address boundary.
Address	Name	Description
0x000000	IMEM_REG	Internal block ram register (bank index)
0x000008	LOCKED	DCM lock status
0x000010	ADDR_REG	Memory page address register
0x000018	MEM_REG	Memory access register (bank, internal/external)
0x000020	IER	Interrupt enable register
0x000028	ISR	Interrupt status register

0x000800	CONTROL_0	Reset, Start, Stop, Run, LoadPhaseTable, LoadSwitchTable,TimingMaster,TimingTerminate,Running,Error (RW)
0x000808	CYCLE_0	The current cycle number (RO) (Could be RW ?)
0x000810	TIME_0	The current cycle time in ms (RO) (could be in us)
0x000818	TEST_0	Sets test parameters (RW)

0x000840-0x000868	Pick Up Channel 1 registers. Same as for Pick Up channel 0
0x000880-0x0008A8	Pick Up Channel 2 registers. Same as for Pick Up channel 0

0x200000:0x3FFFFF	MEMORY	Memory window. 64 bits wide, suitable for slave mode DMA access

The system memory is organised as follows:
Bank	Address	Description
DDR 0	0x00000000	Channel 0 data
DDR 1	0x00000000	Channel 1 data
DDR 2	0x00000000	Channel 2 data
DDR 3	0x00000000	Test data

BlockRAM	0x00000000	Cycle Information table channel 0
BlockRAM	0x00001000	Timing Phase Table channel 0. This is loaded into the systems block ram on the LoadPhaseTable command.
BlockRAM	0x00002000	Timing Switch Table channel 0. This is loaded into the systems block ram on the LoadSwitchTable command

BlockRAM	0x00004000	Cycle Information table channel 1
BlockRAM	0x00005000	Timing Phase Table channel 1. This is loaded into the systems block ram on the LoadPhaseTable command.
BlockRAM	0x00006000	Timing Switch Table channel 1. This is loaded into the systems block ram on the LoadSwitchTable command.

BlockRAM	0x00008000	Cycle Information table channel 2
BlockRAM	0x00009000	Timing Phase Table channel 2. This is loaded into the systems block ram on the LoadPhaseTable command.
BlockRAM	0x0000A000	Timing Switch Table channel 2. This is loaded into the systems block ram on the LoadSwitchTable command.
BlockRAM	0x00010000	Cycle Timing table (8KBytes)

The Register bit definitions are:
Name	Bits	Description
Control.Reset	0	Resets the Pick Up channel
Control.Run	1	Starts the Pick Up channel running
Control.Start	2	Manual start cycle
Control.Stop	3	Manual stop cycle
Control.LoadPhaseTable	4	Loads the new phase table on next system clock edge. (Probably just swaps between two tables)
Control.LoadSwitchTable	5	Loads the new switch table on next system clock edge. (Probably just swaps between two tables)
Control.TimingMaster	6	Sets the logic to connect the digital timing signals to the timing bus. Used on the card connected to the digital timing signal input panel.
Control.TimingTerminate	7	Sets the logic to terminate the timing bus. Used in the last card on the timing bus.
Control.Running	16	System is running (RO)
Control.Error	17	System is in Error (RO)

Test.TestOutput	0-3	Selects the signal which will be output on the channels digital output connector. 0 – none, 1 – generated FREF.
Test.DataSource	4	Selects input data source from DDR3 bank rather than from ADC’s for testing
Test.ClockSource	5	Selects internal 10MHz clock rather than digital input system clock
Test.FRefSource	6	Selects internal Fref source (477 Khz ?)
Test.CycleStart	16	Timing bus signal
Test.CycleStop	17	Timing bus signal
Test.CalStart	18	Timing bus signal
Test.CalStop	19	Timing bus signal
Test.Injection	20	Timing bus signal
Test.HChange	21	Timing bus signal
Test.TimingDrive	31	Sets the board to drive the systems timing bus with the values in this register

The table sizes are as follows:
Table	Size	Time
Cycle Data table	256 MBytes actual used size rounded down to be a multiple of 6 bytes the data entry size	4.46 seconds 21 bunches
Cycle timing table	17840 Bytes. Each entry is 8 bytes. Does this need to be bigger to allow the system to be set to capture single bunches with more past data held in the Cycle Data table ?	4.46 seconds 21 bunches
Cycle Information table	64 Bytes for 8 Cycles of information
Timing Phase Table	512 Bytes
Timing Switch Table	8 Bytes for an 8 x 8 bit matrix

# Synchronisation and Timing
One of the major aspects of the PUPE is its synchronisation system. The synchronisation system produces internal timing signals for the PUPE based on external timing signals and the analogue Sigma data source. Each Pick-Up Channel has the following input timing signals:
Name	Description
SYSTEM_CLOCK	Master 10MHz system clock. The ADC’s 125 Mhz sampling clock will be synchronised to this clock and all of the digital timing signals, except the Injection signal, will re-synchronised to this clock within each FPGA
FREF	Reference frequency. (Up to 477KHz)
CYCLE_START	Start of a machine cycle
CYCLE_STOP	End of Last Flat Top, effectively end of cycle
CAL_START	Start of calibration period
CAL_STOP	End of calibration period
INJECTION	Injection
H_CHANGE	Harmonic changes
SPARE	Spare input not used
SIGMA	The amplitude of the signal from the pick up. This is an analogue signal

There are two tables to control the synchronisation process. A phase table and a switch table. The phase table consists of an 512 element array of 8 bit values. The switch table is an 8 x 8 bit matrix. These tables can be loaded by software at any time before, after or during a processing cycle. The software loads the table via the shared memory interface and then sets an appropriate bit in the CONTROL register to load the table. The following shows a typical set-up of the switch table.
	CYLE_START	CAL_START	CAL_STOP	INJECTION	H_CHANGE	CYCLE_STOP	SPARE
Clear Switches	*		*			*
Clear C-timer	*
Start Acquisition		*		*
Stop Acquisition			*			*
LO Toggle			*	*	*
Gate/BLR / Toggle			*		*
RF Toggle			*	*

# Interrupts
Interrupts can be generated on each of the following events:
Event	Interrupt Bit	Description
CycleStart	0	A processing cycle has started
CycleEnd	1	A processing cycle has completed

# Data Access
Access to the data from the PUPE is provided through a shared memory interface. To reduce the shared memory access window a simple 2MByte paged system is used to access the FPGA’s block RAM and on-board DDR. The on-board DDR is organised as four banks of 256 Mbytes. Within this memory is stored the main data tables for each of the Pick-Up channels and a timing table.
Each of the Pick-Up channels has its own data table stored within its own bank of 256MBytes of DDR. The format of this data table is a circular buffer of Sigma, DeltaX and DeltaY16bit signed values in little endian order. The data table can contain many cycles of data.
0	2	4	6	8	10	12
Sigma	DeltaX	DeltaY	Sigma	DeltaX	DeltaY	...

In the separate fourth bank of memory there is a Cycle Timing table. This circular buffer consists of one timing entry per millisecond. Each entry in the timing table contains a 32bit unsigned “Cycle Number” field and a 32bit unsigned memory address. An entry is made in the timing table every millisecond. The memory address points to offset in the data table which contains data for that time.
0	4	8	16	20
Cycle Number	Data Address	Cycle Number	Data Address	....

There is a Cycle Information table, contained within the fourth bank of memory which contains the positions of start of cycle in the timing table for up to 4 cycles.
Address	Value
0	Cycle Number
4	Timing Address
8	Cycle Number
12	Timing Address
16	Cycle Number
20	Timing Address
24	Cycle Number
28	Timing Address

# Notes
- The C-Timer could be implemented as a microsecond counter. This would give the ability for more accurate timing for future developments.
- May need counter to trigger CycleStop if CERN do not supply CYCLE_STOP timing signal.
- Could store microsecond time in the data table. This would increase memory requirements but would give more accurate timing information.
- Might need a phase delay register. This could be set depending of the position of the Pick-Up in the ring and be used to offset the input from the Fref timing input.
- We might want the ability for the FPGA to DMA a selected pattern of data to the host. For example select the data for bunch 1 and copy that data to the host. This would be to improve the performance of the data retrieval.
- The Cycle Timing table might want to be bigger to allow the system to be set to capture single bunch data over a longer time period.
- One thing we will have to consider is how fast we need to get at the data in memory. CERN will want to be able to take out a selection of data before the next machine cycle. With the paging registers, the table indirection (Cycle Timing to Data) and the fact that they may only want 6bytes here and there over a PCI bus this may be slow. We thus may need to add a data gathering facility in the FPGA itself such as a function that would DMA every 21st set of 6byte samples stating from a given address to the host.
- Another option on the data, as we have more memory that the original spec, is to store data timing information with the data itself rather than have a separate table. We could packetise the data with a simple header containing the channel number and time followed by 21 sets of Sigma/DeltaX/DeltaY data. This would make finding a particular time a bit harder/slower but we could store more accurate times on the data.